## Slide 1
User Motion Brushing
Sensing System
Motion tracking
Pressure Sensor/Proximity Sensor
Processing Unit
Coverage algorithm
Microcontroller
Quadrant timer
Feedback System
- Vibration alerts
Bluetooth Module
- Sends data to mobile app
Mobile App
Displays brushing coverage
Shows brushing history and time spent on each quadrant

## Slide 2
User starts brushing
Sensor receives data
Motion
Pressure
(Relative) Proximity
Data Processing (real-time)
Estimate brush position
Determine coverage areas
Determine time spent on each quadrant
Detect pressure applied
Real-time Feedback
Vibration alerts for missed spots or overpressure
Data Transmission
- Sends data to mobile app
Mobile App
Brushing coverage map
Brushing pressure
Time spent on each quadrant

## Slide 3
Function | Option
Motion Detection | Ultrasonic proximity sensor
Surface Coverage | Optical sensor
Quadrant Timing | Timer with vibration or sound alerts
Pressure Sensing | Pressure sensor
Data Collection | BLE to app
Real-time Feedback | Real-time vibration
Display | Mobile app display
Data Visualization | Heatmap and brushing details

## Slide 4
Hazard | Solution
Sensor failure | Implement auto-calibration routines, alerts for maintenance
Waterproof seal deterioration | Use durable and possibly replaceable seals
Battery degradation | Use long-life batteries, replaceable or recyclable batteries
Hazard | Solution
Compatibility issues | Enable compatibility testing with major OS versions
Outdated firmware | Enable automatic updates through the app
Hazard | Solution
Cracks in hardware | Use impact-resistant materials, include warning if case or hardware is damaged
Loose components | Use vibration-resistant fasteners

## Slide 5
Hazard | Solution
Improper maintenance | Reminders for users to replace brush heads
Overcharging or improper charging | Use LED display to show correct or incorrect charging and include charging indicators and alerts
Hazard | Solution
High or low humidity or temperature | Shut down device when thermal sensor detect unsafe temperatures
Continuously power | Auto-shut down the device after a while of unuse

## Slide 6
Potential Hazards | Social Impacts
Improper disposal of electronics | Create a recycling program for old toothbrush heads and electronics
Battery pollution | Provide recycling instructions or provide drop-off locations for old battery disposal
Users without smartphones | May develop a separate device with core features that displays sensing, timer, and guidance
Overreliance on the device | Provide disclaimer that this device is just for proper brushing, cannot replace dental visits
Comparison pressure | Use private progress data logs instead of public leaderboards of brushing score, or other measures.
High cost | The Smart Toothbrush may be costly with the incorporations of sensors and different hardware. We can develop a low-end version of the toothbrush with less features and more accessible and cheaper for people.